## Slide 1: CacheZoom: How SGX Amplifies The Power of Cache Attacks
Ahmad Moghimi, Gorka Irazoqui, Thomas Eisenbarth
September 26, 2017
CHES 2017 - Taipei

## Slide 2: Intel Software Guard Extensions (SGX)
Trusted Execution Environment
Enclave: Hardware protected user-level software module
  Loaded by the user program
  Mapped by the Operating System
  Authenticated and Encrypted by CPU
Protects against system level adversary
“no protection against access pattern leakages”
New Attacker Model:
Attacker gets full control over OS
Hardware
Hypervisor
OS
App
App
App
blocked
blocked

## Slide 3: Side Channel Attacks on SGX
OS initiated attacks are powerful:
Page Accesses [XCP15, vBWK+17]
Branch Shadowing [LSG+17]
Cache Attacks
  Classic [GESM17, BMD+17]
  Enclave to Enclave [SWG+17]
[XCP15] Yuanzhong Xu, Weidong Cui, Marcus Peinado. Controlled-channel attacks: Deterministic side channels for untrusted operating systems. IEEE S&P, 2015.
[vBWK+17] J. Van Bulck, N. Weichbrodt, R. Kapitza et al. Telling Your Secrets without Page Faults: Stealthy Page Table-Based Attacks on Enclaved Execution. Usenix Security 17.
[LSG+17] Sangho Lee, Ming-Wei Shih, Prasun Gera, et al. Inferring Fine-grained Control Flow Inside SGX Enclaves with Branch Shadowing. Usenix Security 17.
[GESM17] Götzfried, J., Eckert, M., Schinzel, S., Müller, T.: Cache Attacks on Intel SGX. EUROSEC 17
[BMD+17] Ferdinand Brasser,, Urs Müller, Alexandra Dmitrienko et al. Software Grand Exposure: SGX Cache Attacks Are Practical. WOOT 17
[SWG+17] Schwarz, M., Weiser, S., Gruss, D., Maurice, C., Mangard, S: Malware guard extension: Using SGX to conceal cache attacks. DIMVA 2017
SGX Enclave

## Slide 4: Why CacheZoom?
Cache Attacks
Versatile and well-studied
Most libraries have some level of protection by now
High resolution attack:
  spatial resolution: 64b
  page faults: 4kb
CacheZoom
maximizes temporal and spatial resolution on SGX
Breaks implementations and “countermeasures”
Unless cache accesses profile is constant

## Slide 5: How To CacheZoom

## Slide 6: CacheZoom: Cache Isolation
Manipulate OS to reduce noise:
Fix CPU Frequency → stable access times
Kernel task scheduler isolates cores  L1 Cache attack
Core 1
L1$
Last Level Cache (shared)
Core 0
L1$
Victim Enclave
Attacker task
Other Task 0
Other Task 1
Other Task 0
Other Task 1

## Slide 7
CacheZoom:Maximize Resolution
Steps:
Prime entire L1D
Interrupt execution
Probe reload time
re-prime
L1D Cache 4-way s-a.
Set 0
2
63
1
4
3
Execute enclave
Resume execution
Prime+Probe entire L1D
Interleaved Execution
Clean detection of number of set accesses

## Slide 8: CacheZoom: Raw Measurement

## Slide 9: CacheZoom: Noise Filtering
Probe cycles based on the number of evictions
Context-switch noise:
  unavoidable but predictable
  evictions/set caused by an empty enclave

## Slide 10: CacheZoom: Noise Filtering
Probe cycles based on the number of evictions
Context-switch noise:
  unavoidable but predictable
  evictions/set caused by an empty enclave
Filtering the predicted eviction noise

## Slide 11: CacheZooming AES

## Slide 12: Attack Scenario
Attack on AES encryption/decryption:
4 T-Tables: 4x1kB: fills 1 way of entire L1D cache
Huge T-Table: 1x2kB: 64-bit entries w/read offset
S-Box 256 byte table
  only 4 cache lines: 40 accesses each
Assumptions:
Full access to OS resources
AES code & key protected by SGX Enclave
Cipher input or output known

## Slide 13: CacheZoom on AES T-Table
Out of order Execution:
  Repeat accesses to same set
blind sets

## Slide 14: Key Recovery
Known Plaintext attack on first round [TOS10,AGM16]
  Reveals 64-80 key bits
Reconstruct access order
  Difficult due to out-of-order execution
  Arithmetic mean of accesses is reasonable approximation
[TOS10] Eran Tromer, Dag Arne Osvik, Adi Shamir. Efficient Cache Attacks on AES, and Countermeasures. Journal of Cryptology, 2010.
[AGM16] Ashokkumar, C., Giri, R.P., Menezes, B.: Highly efficient algorithms for aes key retrieval in cache access attacks. Euro S&P 2016.

## Slide 15: Prefetching to prevent cache attacks?
Cache warming:
Prefetch or postfetch entire T-table
Once or every round
Works if attacker cannot interrupt AES
  Resistant to previous cache side-channels
  Vulnerable to our attack

## Slide 16: AES S-Box Implementation
256 bytes S-Box tabledifficult
  spans 4 cache lines: 16 access per round
  order? Out of order execution and repeat accesses
  “Secure” if not able to interrupt
Observed # of accesses/set correlated to expected

## Slide 17: AES S-Box Implementation
Correlate accesses/set to observation
Using 1500 traces:

## Slide 18: Where to find them?
Library | Vulnerable Implementations
OpenSSL 1.1.0f | aes_core.c T-table, aes_x86core.c Large T-table; S-box and prefetching configurable
WolfCrypt 3.11.0 | aes.c: T-Table; prefetching before 1st round.
Nettle Mozilla 3.3 | rijndael.c T-Table and S-box configurable
NSS 3.30.2 | aes-encrypt-internal.asm T-table
Libtomcrypt 1.17 | aes.c: T-Table
Libgcrypt 1.7.7 | rjindael.c: T-Table; S-box for last round w/ prefetching
MbedTLS 2.4.2 | aes.c: T-Table; S-box for last round
Implementations configurable through compile or runtime settings

## Slide 19: CacheZoom: High Resolution Cache Attack on SGX
Prime+Probe on L1D w/ interrupted execution
Full Cache image every few instructions
Sample Target: AES
  All table-based implementations vulnerable even with cache warming countermeasure
  Key after <20 traces because of resolution
Side-channels are devastating in SGX
  Constant execution flow+data accesses are essential when processing secrets

## Slide 20
Download CacheZoom at:
  https://github.com/vernamlab/CacheZoom
Thank you!
thomas.eisenbarth@uni-luebeck.de
its.uni-luebeck.de vernam.wpi.edu
@vernamgroup

## Slide 21: How to AES?
T-Tables:
Fast in SW
Data-dependent
vulnerable
S-Box:
Slow
Attack difficult but possible
Fix: always access all (4) cache lines
No Tables:
SIMD [Ham09]
AES-NI or AES co-processor
[Ham09] Mike Hamburg: Accelerating AES with Vector Permute Instructions. CHES, 2009
Other Cryptosystems:
Only secure if data accesses and execution flow constant (or secret-independent)

## Slide 22: Key Recovery
Known Ciphertext attack on last round
  Reveals all key bits after few observations
Attack on 2 last rounds:
  Fewer observations (1 with ideal leakage; 2-3 is practical)
  Increased computational load (2h with python as of now)