## Slide 1
FPGA-based Key Generator for the Niederreiter Cryptosystem using Binary Goppa Codes
Wen Wang1, Jakub Szefer1, and Ruben Niederhagen2
Yale University, USA
Fraunhofer Institute SIT, Germany
Sep 26, 2017

## Slide 2
Code-based cryptography
Public-key cryptography
Classic
Post-quantum
Lattice-based
Code-based
Niederreiter
McEliece
Binary Goppa code
GRS code
…
...
...
Notes: Add …

## Slide 3
Code-based cryptosystem
Key generator
Encryption
Decryption
Modules in a code-based cryptosystem
Key generator
  no existing hardware work with 266-bit security
  complex in logic and cycles
  hardware implementation needed: HSM, smart cards and etc.
Encryption
  cheap in hardware
Decryption
  a few related works: Shoufan’10, Heyse’12, Ghosh’14, and etc.
(sk, pk)
pk
sk

## Slide 4
PQCRYPTO project recommendation in 2015
  266-bit security
  system parameters
    field size m = 13
    number of correctable errors t = 119
    code length n = 6960
  public key ~ 1MB
  secret key ~ 13kB
Parameters for code-based cryptosystem
Design | Scheme |  |  |  | Security Level | PK Size | Modules
Shoufan’10 Heyse’12 Ghosh’14 Our work | McEliece Niederreiter McEliece Niederreiter | 11 11 12 13 | 50 27 66 119 | 2048 2048 3307 6960 | 103-bit 80-bit 128-bit 266-bit | 100 kB 63 kB 243 kB 1 MB | Key./Enc./Dec. Enc./Dec. Enc./Dec. Key.
Design | Scheme |  |  |  | Security Level | PK Size | Modules
Shoufan’10 Heyse’12 Ghosh’14 Our work | McEliece Niederreiter McEliece Niederreiter | 11 11 12 13 | 50 27 66 119 | 2048 2048 3307 6960 | 103-bit 80-bit 128-bit 266-bit | 100 kB 63 kB 243 kB 1 MB | Key./Enc./Dec. Enc./Dec. Enc./Dec. Key.

## Slide 5
Binary Goppa code
  degree- Goppa polynomial
  code locator
  can be defined by a parity check matrix , e.g.,
Niederreiter encrypt
  compute syndrome
Niederreiter decrypt
  compute given the syndrome S
Coding theory
Notes: point out in this slide which is secret key and which is public key

## Slide 6
Input: System parameters: and .
1: Choose a random sequence of distinct elements in
2: Choose a random polynomial such that for all
3: Compute the parity check matrix
4: Transform to a binary parity check matrix
5: Transform into its systematic form
6: Return the private key and the public key
Key generator algorithm
Notes: Move diagram over to the end

## Slide 7
Solving systems of linear equations; Matrix systemization
Gaussian elimination
Systolic architecture
forward
backward
forward & backward
Gaussian systemizer
Notes: add 2010-paper old figures

## Slide 8
Performance of the Gaussian systemizer for a matrix
Number in BLUE shows result of the best TimeArea
Performance of the Gaussian systemizer for a matrix
 | Cycles | Logic | TimeArea | Mem. | Reg. | Fmax(MHz)
10 20 40 80 160 320 | 150,070,801 38,311,767 9,853,350 2,647,400 737,860 208,345 | 826 1325 3367 10,983 40,530 156,493 | 1.241011 5.081011 3.321010 2.911010 2.991010 3.261010 | 663 666 672 680 720 848 | 678 1402 4642 14,975 55,675 213,865 | 257 276 297 296 290 253
 | Cycles | Logic |  | Mem. | Reg. | Fmax(MHz)
10 20 40 80 160 320 | 150,070,801 38,311,767 9,853,350 2,647,400 737,860 208,345 | 826 1325 3367 10,983 40,530 156,493 |  | 663 666 672 680 720 848 | 678 1402 4642 14,975 55,675 213,865 | 257 276 297 296 290 253
 | Cycles | Logic | TimeArea | Mem. | Reg. | Fmax(MHz)
1 2 4 | 922,123 238,020 63,300 | 2539 5164 10,976 | 2.34109 1.23109 6.95108 | 14 14 13 | 318 548 1370 | 308 281 285
 | Cycles | Logic |  | Mem. | Reg. | Fmax(MHz)
1 2 4 | 922,123 238,020 63,300 | 2539 5164 10,976 |  | 14 14 13 | 318 548 1370 | 308 281 285
Performance

## Slide 9
Multipoint polynomial evaluation
horner scheme
characteristic-2 additive FFT
  radix conversion:
  twisting
  reduction
Gao-Mateer additive FFT

## Slide 10
Performance of additive FFT using different numbers of multipliers
(evaluating a degree-119 polynomial at all data points in )
Twisting
Radix
Conversion
g(x)
f(βx)
(f0, f1 )
Reduction
data memory
const. memory
= f(x)
Design | Multipliers Twist Reduction | Cycles | Logic | TimeArea | Mem. | Reg. | Fmax
add_FFT | 4 32 8 32 16 32 32 32 | 1188 1092 1044 1020 | 11,731 12,095 12,653 14,049 | 1.39107 1.32107 1.32107 1.43107 | 63 63 63 63 | 27,450 27,470 27,366 26,864 | 399 MHz 386 MHz 373 MHz 322 MHz
horner | 32 | 30,720 | 3478 | 1.07108 | 0 | 2085 | 270 MHz
Design |  | Cycles | Logic |  | Mem. | Reg. | Fmax
add_FFT | 4 32 8 32 16 32 32 32 | 1188 1092 1044 1020 | 11,731 12,095 12,653 14,049 |  | 63 63 63 63 | 27,450 27,470 27,366 26,864 | 399 MHz 386 MHz 373 MHz 322 MHz
horner | 32 | 30,720 | 3478 |  | 0 | 2085 | 270 MHz
Non-recursive hardware implementation

## Slide 11
Random, uniform permutation
Algorithm
Hardware implementation
Performance for shuffling elements
Initialize: A = {0, 1, …, n-1}
for i from n-1 downto 0 do
Generate j uniformly from range[0, i]
Swap A[i] and A[j]
Output: Shuffled array A
m | Size (= 2m) | Cycles (avg.) | Logic | TimeArea | Mem. | Reg. | Fmax(MHz)
13 | 8192 | 23,635 | 149 | 3.52106 | 7 | 111 | 335
m | Size (= 2m) | Cycles (avg.) | Logic |  | Mem. | Reg. | Fmax(MHz)
13 | 8192 | 23,635 | 149 |  | 7 | 111 | 335
PRNG
Fisher-Yates
Shuffle
dual-port
memory
Fisher-Yates Shuffle

## Slide 12
Key generator

## Slide 13
Performance results
(m = 13, t = 119, n = 6960)
case |  |  | Cycles | Logic | TimeArea | Mem. | Fmax | Time
Altera Stratix V |  |  |  |  |  |  |  | 
logic bal. time | 40 80 160 | 1 2 4 | 11,121,220 3,062,942 896,052 | 29,711 48,354 101,508 | 3.301011 1.481011 9.101010 | 756 764 803 | 240 MHz 248 MHz 244 MHz | 46.43 ms 12.37 ms 3.68 ms
case |  |  | Cycles | Logic |  | Mem. | Fmax | Time
Altera Stratix V |  |  |  |  |  |  |  | 
logic bal. time | 40 80 160 | 1 2 4 | 11,121,220 3,062,942 896,052 | 29,711 48,354 101,508 |  | 756 764 803 | 240 MHz 248 MHz 244 MHz | 46.43 ms 12.37 ms 3.68 ms
Xilinx Virtex UltraScale+ |  |  |  |  |  |  |  | 
logic bal. time | 40 80 160 | 1 2 4 | 11,121,220 3,062,942 896,052 | 42,632 60,989 112,845 | 4.741011 1.871011 1.011011 | 348.5 356 375 | 200 MHz 221 MHz 225 MHz | 55.64 ms 13.85 ms 3.98 ms
Xilinx Virtex UltraScale+ |  |  |  |  |  |  |  | 
logic bal. time | 40 80 160 | 1 2 4 | 11,121,220 3,062,942 896,052 | 42,632 60,989 112,845 |  | 348.5 356 375 | 200 MHz 221 MHz 225 MHz | 55.64 ms 13.85 ms 3.98 ms
Design |  |  |  | Cycles (avg.) | Freq. | Time (avg.) | Arch.
Shoufan’10 Our work | 11 11 | 50 50 | 2048 2048 | 1.47107 2.72106 | 163 MHz 168 MHz | 90 ms 16 ms | Virtex V Virtex V
Design |  |  |  | Cycles (avg.) | Freq. | Time (avg.) | Arch.
Shoufan’10 Our work | 11 11 | 50 50 | 2048 2048 |  | 163 MHz 168 MHz | 90 ms 16 ms | Virtex V Virtex V
Chou’17 Our work | 13 13 | 128 128 | 8192 8192 | 1.24109 4.30106 | 1-4 GHz 215 MHz | 1236-309 ms 20 ms | Haswell Stratix V
Chou’17 Our work | 13 13 | 128 128 | 8192 8192 |  | 1-4 GHz 215 MHz | 1236-309 ms 20 ms | Haswell Stratix V

## Slide 14
Conclusions
Building blocks
  Gaussian Systemizer
  any large-sized matrix, any binary field
  Gao-Mateer additive FFT
  takes around 1000 cycles for evaluating a degree-119 polynomial at points
  Fisher-Yates Shuffle
  uniform, cheap in logic
Secret key generation
  Gaussian Systemizer, Fisher-Yates Shuffle
Public key generation
  Gaussian Systemizer, Gao-Mateer additive FFT
First hardware-based key generator with 266-bit security level
Produce a key pair for parameters m = 13, t = 119, and n = 6960 in ms
Notes: Change all 128 -> 266, all **-security

## Slide 15
Thanks!
http://caslab.csl.yale.edu/code/keygen/