## Slide 1: Hardware Masking, Revisited
Maik Ender
Amir Moradi
September 11 - CHES 2018 - Amsterdam
Thomas De Cnudde

## Slide 2
The idea is to build a model for the physical characteristics of a device,
and then design masking schemes with provable security in that model
We checked the influence of these parameters on the leakage

## Slide 3: What do we control in the measurement setup and in the implementation?
Supply Voltage
Shunt Resistor
Distance between the shares
Temperature
Circuit Size
Clock Frequency
Number of Shares

## Slide 4: Hardware Masking, Revisited
3
Conclusions
- Summary
- Implications
2
Can we make Masked Implementations leak?
1
Experiments on
a Toy Example
to reveal the influence of the various parameters
on the leakage
Notes: We end with a conclusion where we summarise our findings and discuss the implications of our work

## Slide 5: Hardware Masking, Revisited
3
Conclusions
2
Can we make Masked Implementations leak?
1
Experiments on
a Toy Example
revealing the influence on the leakage by
1. the various parameters
2. coupling of FPGA wires

## Slide 6: One share in our toy example consists of consecutive MixColumn modules
We can choose between
a lower power consumption from 3 MCs
a higher power consumption from 6 MCs

## Slide 7: Four iterated MixColumns shares are placed next to each other and in full isolation
We can test the influence of the number of shares
and the distance between the shares on the leakage
Notes: Using the Isolated Design Flow (IDF) of Xilinx

## Slide 8: Supply Voltage & Shunt Resistor
Vdd 1.0v, 1.0Ω
Vdd 1.0v, 0.0Ω
Vdd 1.2v, 1.0Ω (Sakura-G default)
Vdd 1.2v, 0.0Ω
Vdd 1.3v, 0.0Ω
max(|t-statistic|)
Number of Traces
100M
80M
60M
40M
20M
12
10
8
6
4
2
Fixed-vs-random t-test
iterated_MC1 and iterated_MC4
3 MCs active
6MHz
21°C
The higher the supply voltage,
the higher the leakage
The lower the shunt resistor,
the higher the leakage

## Slide 9: Distance
Iterated_MC1↔2
Iterated_MC1↔3
Iterated_MC1↔4
Fixed-vs-random t-test
3 MCs active
6MHz
Vdd 1.2v, 0.0Ω , 21°C
The distance between the shares
does not influence leakage much
max(|t-statistic|)
Number of Traces
100M
80M
60M
40M
20M
8
6
4
2

## Slide 10: Temperature
21°C
50°C
70°C
max(|t-statistic|)
Number of Traces
100M
80M
60M
40M
20M
15
10
5
Fixed-vs-random t-test
iterated_MC1 and iterated_MC4
3 MCs active
6MHz
Vdd 1.3v, 0.0Ω
The higher the temperature,
the higher the leakage
Notes: Quality of the randomness is not altered by the temperature

## Slide 11: Circuit Size and Clock Frequency
15
10
5
20
3MC, 6MHz
3MC, 48MHz
6MC, 6MHz
6MC, 48MHz
Fixed-vs-random t-test
iterated_MC1 and iterated_MC4
Vdd 1.3v, 0.0Ω, 21°C
The more MCs active,
the higher the leakage
The higher the peak-to-peak
power consumption,
the higher the leakage
Number of Traces
100M
80M
60M
40M
20M
max(|t-statistic|)
The higher the clock frequency, the higher the leakage

## Slide 12: Number of Shares
max(|t-statistic|)
Number of Traces
200M
150M
100M
50M
15
10
5
2 shares 1,2
3 shares 1 to 3
4 shares 1 to 4
Fixed-vs-random t-test
1st-, 2nd- and 3rd-order masking
6 MCs active
6MHz
Vdd 1.3v, 0.0Ω, 21°C
No 2nd-order leakage in
the 2nd-order secure design
No 2nd- or 3rd-order leakage in
The 3rd-order secure design
All linear 1st-, 2nd- and 3rd-order designs leak in the 1st-order!

## Slide 13: Hardware Masking, Revisited
3
Conclusions
2
Can we make Masked Implementations leak?
1
Experiments on
a Toy Example
revealing the influence on the leakage by
1. the various parameters
2. coupling of FPGA wires

## Slide 14: Does leakage current in open switch transistors contribute to the leakage in FPGAs?

## Slide 15: What is the influence of the leakage current?
Open transistors inside a switch matrix could couple wires from two different shares
What is the influence of the number of shared open switches?

## Slide 16: Our experiments are designed with an increasing number of shared open switches
0
0
0
0
0
0
0
0
20
0
0
0
0
0
20
0
16
0

## Slide 17: We route two wires close to each other in the middle of two iterated_MC shares

## Slide 18: Number of shared open switches
max(|t-statistic|)
Number of Traces
200M
150M
100M
50M
15
10
5
Fixed-vs-random t-test
6 MCs active
Vdd 1.3v, 0.0Ω, 6MHz, 21°C
Routing does not have much eﬀect on the observed leakage
20
original
0 shared open switches
20 shared open switches
20+16 shared
open switches

## Slide 19: Hardware Masking, Revisited
3
Conclusions
2
Can we make Masked Implementations leak?
- Threshold Implementation of PRESENT
- Domain-Oriented Masking of AES
- d+1 Threshold Implementations of AES
1
Experiments on
a Toy Example

## Slide 20: A Threshold Implementation of PRESENT
max(|t-statistic|)
Number of Traces
200M
150M
100M
50M
2
Vdd 1.3v, 0.0Ω
Vdd 1.0v, 1.0Ω
4
6
8
1st-order implementation with 3 shares leaks in the 1st order
Fixed-vs-random t-test
8 rounds of encryption
12MHz
21°C
PRESENT-80 TI from [PMK+11]

## Slide 21: Masked AES implementations with d+1 shares
Number of Traces
100M
80M
60M
40M
20M
DOM, 2 shares
DOM, 3 shares
d+1 TI, 2 shares
d+1 TI, 3 shares
max(|t-statistic|)
2
4
6
8
10
Fixed-vs-random t-test
full encryption
24MHz
Vdd 1.2v, 1.0Ω, 21°C
Domain-Oriented Masking from [GMK16]
d+1 TI from [DRB+16]
All 1st- and 2nd-order designs
leak in the 1st-order!
Notes: Second order leakage: t=200 for 2 share implementations
Third order leakage: t=10 for 3 share implementations

## Slide 22: Hardware Masking, Revisited
3
Conclusions
2
Can we make Masked Implementations leak?
1
Experiments on
a Toy Example
- Summary
- Implications

## Slide 23: Hardware Masking, Revisited
Can we make Masked Implementations leak?
YES!

## Slide 24: Summary for the Spartan-6 FPGA
Higher leakage with
  higher supply voltages
  lower shunt resistors
  higher temperatures
  higher peak-to-peak power consumption (higher clock frequency or larger circuits)
  lower number of shares
Leakage does not depend much on
  the distance between the shares
  the leakage current from open transistors between the shares

## Slide 25: Implications
Assumptions can be violated! Not surprising, e.g. glitches, early signal propagation
Correctly masked implementations leak? Yes, with a high number of traces in a low noise environment
Can this be exploited by an attacker? How?
What about ASICs? Likely more traces needed…

## Slide 26: Potential Solutions
Temporal non-completeness?
  Don’t process on more than d shares per clock cycle for dth-order security Expensive…
Embedded voltage regulators?
  Do EM signals show similar issues?
Sharing the Vdd lines? Not clear how to apply nonlinear functions in this setting…
Use the leakage detection in addition to attacks?
  Moments-Correlating DPA [MS16]

## Slide 27
September 11 - CHES 2018 - Amsterdam