## Slide 1: Side-Channel Attacks on Post-Quantum Signature Schemes based on Multivariate Quadratic Equations
11. Sep. 2018
Aesun Park1 , Kyung-Ah Shim2*, Namhun Koo2, and Dong-Guk Han1
1Department of Financial Information Security, Kookmin University, Seoul, Republic of Korea 2Division of Mathematical Modeling, National Institute for Mathematical Sciences, Daejeon, Republic of Korea
Notes: Hi Everyone.
I am Aesun Park from kookmin university.
I’m so glad to talk in CHES.
Today, I’ll talk about the side-channel vulnerability / on UOV variants(베리언스).
This is joint work with NIMS.

## Slide 2
1999 UOV
2005 (General) Rainbow : a layered MQ-signature scheme based on UOV
2012 (Efficient) Rainbow & UOV
EUROCRYPT
ACNS
CHES
Rainbow
UOV
Efficient Implementations in HW/SW
2006 efficient software implementations
SAC
Reduction in the size of the public key
2017 Lifted UOV
INDOCRYPT
UOV Variants Signature schemes
Czypek et al.
Beullens et al.
It uses the linear map T of CHES form
Improving efficiency and reducing the key sizes
For smaller UOV public keys
reducing the key space and runtime
removing the constant part
Appling linear maps like the picture
CHES form
Notes: In 1999, UOV has been proposed in EUROCRYPT.
And then, In 2005(two thousand five), general Rainbow, which is a layered MQ-signature scheme based on UOV, has been proposed to improve efficiency and reduce the key sizes.
Since the study on efficient software implementations was proposed in 2006,
there have been many studies on efficient implementation in hardware and software.
In CHES 2012(twenty twelve),/ Czypek(씨펙) et al. / demonstrated the feasibility(피~즈빌리티) of MQ-signature schemes / on an 8-bit AVR micro-processor.
They removed the constant part of the linear maps / and applied linear maps like the picture / to reduce the key space and runtime.
We call this shape CHES form.
In 2017, Beullens(비얼렌즈) et al. proposed a Lifted UOV for Smaller UOV Public Keys.
it uses the T of CHES 2012(twenty twelve) form.
(like this, 포인터로 가르키며)

## Slide 3
1998 Simple Power Analysis
Differential Power Analysis
2004 Correlation Power Analysis
1996 Timing Attacks
2017 Semi-invasive Attack on enTTS
The Computer Journal
SCA on UOV Variants Signature schemes
Implementations of post-quantum algorithms are vulnerable to PA
2018 Ours
CHES
Non-invasive Attacks on Rainbow and UOV
The studies of PA against UOV variants lack.
Yi et al.
Paul Kocher
Notes: After Paul Kocher proposed methods of finding keys / using Time and Power and so on,
Power Analysis has been carried out for many crypto algorithms.
It is not surprising / that implementations of post-quantum algorithms are vulnerable to PA.
Therefore, may studies for PA vulnerability of PQC have been studied.
However, the studies of PA against UOV variants lack.
There is only one result except ours.
In 2017(twenty seventeen), / Yi et al. recover the central map F on enTTS / using a fault analysis.
(click)
There is no attack / using only Power Analysis.
Today, I will introduce an non-invasive attack against Rainbow and UOV.

## Slide 4
Signature generation on Rainbow
Secret maps :
Inverse
Inverse
Inverse
M
E
S
E
message
S
S
M
A
8
7
80
2
75
2
12
5
signature
Random values
Solving the linear equations
Linear map
Matrix-vector product over a field
Linear map
Matrix-vector product over a field
Basic operations
Field multiplications & additions
Notes: Here, I’ll briefly explain the signature generation on Rainbow.
There are three secret maps S, F, and T.
signature generation consists of three steps.
(클릭)
The first step is to perform / an inversion linear map of the input message.
At this step, / a matrix-vector product over a field is used(유-즈드).
(클릭)
The second step is to invert / central map F with the transformed message.
At this step, Random values are used and linear equations are solved.
(클릭)
The last one is to apply / an inversion of the(디) other linear map.
It also uses a matrix-vector product over a filed.
(클릭)
Rainbow uses Field Multiplications and additions as the basic operations.

## Slide 5
Inverse
Inverse
Inverse
M
E
S
E
message
S
S
M
A
9
25
14
9
56
40
8
17
signature
Linear map
Matrix-vector product over a field
Linear map
Matrix-vector product over a field
Same Input (message)  Different Output (signature)
Rainbow generates different signatures for the same message.
Random values
Solving the equations
Signature generation on Rainbow
Notes: As I mentioned, the second step uses random values.
Because of this, Rainbow generates different signatures for the same message.
This feature leads to difficulty in power analysis.

## Slide 6
Applicability of Power Analysis
Inverse
Inverse
Inverse
M
E
S
E
message
S
S
M
A
9
25
14
9
56
40
8
17
signature
EASY
Difficult
unknown random values are used
Power analysis uses the position where the fixed secret value and the random public value are computed.
The methods for efficiency can be vulnerable to PA.
Signature generation on Rainbow
Notes: Power analysis generally uses the position / where the fixed secret value and the random public value are computed.
(클릭) So, in the first step, power analysis is easily applied.
(클릭)
However, in the calculation of F, unknown random values are used.
Therefore, the power analysis cannot be easy / because the intermediate values of T can’t be calculated.
However, the methods for efficiency can be vulnerable to Power analysis.

## Slide 7
[Goal] Secret maps recovery on Rainbow and UOV
Rainbow
UOV
The flow of our proposed attacks
START
Does it use the special form linear maps?
CPA on the
YES
NO
CPA on the
Recovery
using , and
END
Recovery and using algebraic KRAs
Sub-attack 1
the general field multiplication vulnerabilities
Sub-attack 2
Sub-attack 3
Notes: Our goal / is to recover the secret maps of the Rainbow and UOV / only using CPA and algebraic key recovery attacks.
We propose two attacks.
For easily explain, I describe three sub attacks.
The first sub-attack exploits the general field multiplication vulnerabilities.
The second one is used / when the linear map T has the form / suggested in CHES 2012(twenty twelve) .
This attack can be used(유즈-드) for UOV as well as for Rainbow.
The last one is used to rainbow with random linear map T after S has been recovered.
우리는 MQ 기반 서명 스킴에서 linear map 연산이 전력 분석에 취약함을 보였다.
이에 따라 공격은 크게 2가지로 나눌 수 있다.
첫번째는 linear map이 CHES 2012에서 제안한 모양을 따를 때 공격 할 수 있는 것으로 random message를 이용하여 S가 연산될때의 전력 파형 수집 후 CPA를 통해 𝑆^(−1)를 복원한다.
이후 서명 값과 T가 연산될 때의 전력 파형을 이용하여 CPA를 이용해 𝑇^(−1)를 복원하고 공개키 P와 S,T를 이용해 나머지 F를 복원한다.
두번째 방법은 일반적인 random linear map을 이용할 때 공격하는 방법으로 𝑆^(−1)의 CPA는 모양에 상관 없이 적용 가능하므로 S 복원 후 algebraic Key Recovery Attack을 이용해 F와 T를 복원한다.

## Slide 8
Environment | 
Target chip | Atmel AVR XMEGA128
Sampling | 7.38 MS/s
Algorithm | Matrix-vector product over GF()
Attack system | 
ChipWhisperer-Lite, 500 traces | 
Implementation | 
8-bit implementation | 
Environment | 
Target chip | Atmel AVR XMEGA128
Sampling | 7.38 MS/s
Algorithm | 
Attack system | 
ChipWhisperer-Lite, 500 traces | 
Implementation | 
8-bit implementation | 
Experimental setup
multiplication each loaded y by the i-th column.
To reduce the number of times y is loaded.
Notes: We implemented(임프리멘티드) the Matrix-vector product on a field GF(two to the power of eight) / and experimented(익스피어리먼티드) with ChipWhisperer-Lite / which is developed(디벨롭티드) for side-channel analysis by collin.
Thanks Collin.
The Algorithm used(유-즈드) in the experiment is (인디 익스페어리먼 이즈) / implemented by multiplying each loaded y / by the i-th (바이 디 아이쓰) column / to reduce the number of times y is loaded.
Power traces were collected using 500 random messages.

## Slide 9
Sub-attack 1
Invert
Intermediate result
Secret
Known
CPA on the
the result of CPA for
Maximum correlation coefficients according to increased number of traces for
: hypothetical key
Notes: CPA on the S is very easy because the attacker can control the message.
Intermediate results are chosen / as the value / multiplied by each element.
For example, / (guess times y1) can be used as an intermediate result to recover (s prime one one).
Here, Guess represents a hypothetical(하이포세티컬) key.
In the same way, after recover ,/ ( times y1 plus guess times y2) is used / as an intermediate result to recover .
This picture shows the result of CPA for s prime one one.
This represents / the maximum correlation coefficients / according to an increased number of traces.
We experimented(익스피어리먼티드) with traces that increase by 10.
CPA on the S is very easy because the attacker can control the message.
Intermediate results are chosen / as the value / multiplied by each element.
For example, / 𝑔𝑢𝑒𝑠𝑠∙𝑦_1 (guess times y1) can be used as an intermediate result to recover 𝑠_11^′(s prime one one).
Here, Guess represents a hypothetical(하이포세티컬) key.
In the same way, after recover 𝑠_11^′,/ 𝑠_11^′∙𝑦_1+𝑔𝑢𝑒𝑠𝑠∙𝑦_2 (𝑠_11^′ times y1 plus guess times y2) is used / as an intermediate result to recover 𝑠_12^′.
This picture shows the result of CPA for s prime one one.
This represents / the maximum correlation coefficients / according to an increased number of traces.
We experimented(익스피어리먼티드) with traces that increase by 10.

## Slide 10
Sub-attack 2
CPA on the
Invert
Matrix-vector product over a field
It is hard to compute X‘
 to compute the intermediate value is difficult
Rainbow
UOV
Notes: Because the last step also uses(유지즈) a matrix-vector product / this part can also be an attack point.
However, / it is hard to compute X‘ which is calculated with T / because we don’t know F even if S is recovered.
It means / that to compute / the intermediate value (디 인어미디에잇 벨-류) is difficult.
If the Rainbow or UOV is used (이즈 유즈-드) CHES form, it is possible to compute the intermediate value(디 인어미디에잇 벨-류) .
So CPA is possible.

## Slide 11
Sub-attack 2
CPA on the
Rainbow
UOV
Signature X
, , ,
(Assume) Special form
Notes: For example, suppose we use a T that looks like this.
We can know the values from to because of the blue square.
That is, , and equal , , , and , respectively(리스펙티블리)
For example, suppose we use a T that looks like this.
And then, 〖x′〗_8 equals x_8.
〖x′〗_7, 〖x′〗_6 and 〖x′〗_5 also equal x_7, x_6, and x_5, respectively(리스펙티블리) / because of the blue square.
Therefore, We can know the values from 〖𝑥′〗_5 to 〖𝑥′〗_8.

## Slide 12
Sub-attack 2
CPA on the
Rainbow
UOV
Signature X
Intermediate result: , ,
(Assume) Special form
Notes: So, now we can attack the green part.
Unlike S, / we can not guess the exact value / because we do not know and .
However, there are positions / where and are multiplied.
We target these positions as an intermediate result.
Knowing these values means / we can attack the green part.
Unlike S, / we can not guess the exact value / because we do not know 〖𝑥′〗_3 and 〖𝑥′〗_4.
However, since there is position / where 〖𝑡′〗_𝑖𝑗 and 〖𝑥′〗_𝑗 are multiplied, / an intermediate result can be used(유즈-드) as a product of two values.

## Slide 13
Sub-attack 2
CPA on the
(Assume) Special form
Rainbow
UOV
Signature X
Compute and
Notes: Now, we have found the green part, / we can compute and .
Therefore, T can be recovered / by finding the blue part as the previous method.
(클릭)
This picture shows the CPA result / for .
As you can see, we could find using 50 traces.
Now, we have found the green part, / we can calculate 〖𝑥′〗_3 and 〖𝑥′〗_4.
Therefore, T can be recovered / by finding the blue part in the same way.
(클릭)
This picture shows the CPA result / for 〖𝑡′〗_45.
This result represents / the maximum correlation coefficients / according to an increased number of traces.
As you can see, we could find the secret element 〖𝑡′〗_45 using 50 traces.

## Slide 14
Sub-attack 2
CPA on the
(Assume) Special form
Rainbow
UOV
the result of CPA for
Maximum correlation coefficients according to increased number of traces for
Notes: This picture shows the CPA result / for .
As you can see, we could find
Now, we have found the green part, / we can calculate 〖𝑥′〗_3 and 〖𝑥′〗_4.
Therefore, T can be recovered / by finding the blue part in the same way.
(클릭)
This picture shows the CPA result / for 〖𝑡′〗_45.
This result represents / the maximum correlation coefficients / according to an increased number of traces.
As you can see, we could find the secret element 〖𝑡′〗_45 using 50 traces.

## Slide 15
Sub-attack 3
Recovery and using algebraic KRAs
(Assume) general form , recovery
Find an equivalent key s.t
The equivalent key and have the form the figures.
Rainbow() = Rainbow(GF(), 36, 21, 22)
0.46 milliseconds
Intel Xeon E5-2687W CPU 3.1 GHz with 256GB RAM
; certain places with zero coefficients in are known
Let ,
Where is the k-th component of the central map .
=
=
No. equations | No. variables
(linear equations) | 
No. equations | No. variables
Notes: Here, I’ll explain a brief description / about the recovery of F and T / using algebraic key recovery attacks.
We assume that S has been found and T has been used the general form.
Because we find the S and know public key p / we can compute .
We let the green p is / and tilde T is inverse T.
green P circle tilde T equals F and certain places with zero coefficients in are known because we have found S and Rainbow has different central maps each layer.
So , we obtain the following equality.
we can find an equivalent key T’ with high probability(프로바빌리티) by solving the equations by finding linear equations with variables.
Therefore we can make a forged signature.
We could find an equivalent key / using this parameter / in less than 0.46(zero point four six) milliseconds / on Intel Xeon CPU.
In this page, I’ll explain a brief description / about the recovery of F and T / using algebraic key recovery attacks.
We assume that S has been found and T has been used the general form.
Because we find the S and know public key p / we can compute 𝑺^(−𝟏)∘𝓟.
We let the green p is 𝑺^(−𝟏)∘𝓟 / and tilde T is inverse T.
As P circle tilde T equals F and certain places with zero coefficients in ℱ^((𝑘) ) are known, we obtain the following equality.
However, this system can’t be solved.
(클릭)
To improve complexity, we can find an equivalent key.
Using equivalent keys like these, we can solve the equations by finding 𝑣_1 𝑜_1 𝑜_2 linear equations with (𝑣_1+𝑜_1 ) 𝑜_2 variables.
(클릭)
We are able to recover equivalent key / using this parameter / in less than 0.46(zero point four six) milliseconds / on Intel Xeon CPU.

## Slide 16
Attack 1 = sub-attack 1 + sub-attack 2
CPA on Rainbow implementation with Equivalent keys in CHES 2012
Similar attack: CPA on UOV implementation with equivalent key
START
Does it use the special form linear maps?
CPA on the
YES
NO
CPA on the
Recovery
using , and
END
Recovery and using algebraic KRAs
Notes: In summary,
The first attack can be used / when the linear maps have the CHES form.
All of the secret keys S, F, and T can be recovered by a combination of sub-attack 1 and sub-attack 2.
That is, After recovering the two linear maps, S and T, using power analysis / we recover the central map F by simple calculation with the public key P.

## Slide 17
Attack 2 = sub-attack 1 + sub-attack 3
Hybrid attack on Rainbow implementation with random linear maps
START
Does it use the special form linear maps?
CPA on the
YES
NO
CPA on the
Recovery
using , and
END
Recovery and using algebraic KRAs
Notes: The second one is a hybrid attack / which uses(유지즈) CPA and algebraic key recovery attacks.
It can attack rainbow-like signature schemes with random linear maps.

## Slide 18
Other MQ-signature schemes
UOV-like single layer schemes.
Rainbow-like multi-layered schemes.
Rainbow and HiMQ-3
[INDOCRYPT 2017] Lifted UOV (LUOV)
Attack 1
LUOV is submitted to NIST for Post-Quantum Cryptography Standardization.
LUOV uses the form of the equivalent key proposed in CHES 2012.
affine-substitution (quadratic)-affine (ASA) structure
GF(),
Attack 2
Notes: Our attacks can apply other MQ-signature schemes.
First, LUOV which is submitted(서브밋티드) to NIST, uses CHES form.
So it can be applied to our proposed attack 1.
Rainbow and HiMQ-3, which use ASA structure and are computed over GF(two to the power of n), also are vulnerable to our attack 2.

## Slide 19
Countermeasures
UOV-like single layer schemes
Use the that is removed the relation between the signature value and the intermediate value.
Rainbow-like multi-layered schemes
Message randomization
Overhead: field multiplications and a field inversion
focus on implementing a secure matrix-vector product against PA
Notes: To avoid our attacks, / UOV-like single layer schemes / should not use the form of the linear map / proposed in CHES 2012(twenty twelve).
in other words, we must use the that is removed the relation between the signature value and the intermediate value.
Rainbow-like multi- layered schemes/ can be recovered all secret maps / if S is recovered.
Therefore, we must focus on implementing(임플리먼팅) a secure matrix-vector product against PA.
we can use message randomization to prevent our in the first step.
That is, multiply all elements of a message by a random number r, / and perform a general matrix-vector product.
And then, we multiply the output of the matrix-vector product / by the inverse r.
We need 2 times m field multiplications and a field inversion.
we also need a random number generation step.
Here, m is the size of the vector.
To avoid our attacks, / schemes that do not use S, such as UOV, / should not use the form of the linear map / proposed in CHES 2012(twenty twelve).
in other words, we must use the 𝑇 that is removed the relation between the signature value and the intermediate value.
The scheme using S like Rainbow / can be recovered all secret maps / if S is recovered regardless(리가드리스) of the use of equivalent keys.
Therefore, we must focus on implementing(임플리먼팅) a secure matrix-vector product against PA.
we can use message randomization to prevent our attack / when inverse S and message are multiplied.
That is, multiply all elements of a message by a random number r, / and perform a general matrix-vector product.
In the final step, we multiply the output of the matrix-vector product / by the inverse r.
We then can avoid our attacks by adding 2 times m field multiplications and a field inversion.
Where m is the size of the vector.

## Slide 20
Conclusion
Our contributions
Further work
More efficient countermeasures
Security analysis against high-order and fault injection attacks
CPA on Rainbow and UOV implementation with equivalent keys in CHES 2012
Hybrid attack on Rainbow implementation with random linear maps
Our attacks can apply to other MQ-signature schemes.
Countermeasure against first-order CPA
Notes: This is a conclusion.
We proposed CPA on Rainbow and UOV with equivalent keys in CHES 2012.
And we also proposed the Hybrid attack on Rainbow implementation with random linear maps using CPA and algebraic key recovery attacks.
Our attacks can apply to other MQ-signature schemes.
We proposed simple countermeasure against first-order CPA.
We’ll study about More efficient countermeasures and about Security analysis against high-order and fault injection attacks

## Slide 21
Notes: That’s all. Thank you for your attention.
Any questions and comments?