## Slide 1: Reconciling d + 1 Masking in Hardware and Software
Hannes Gross, Stefan Mangard
Graz University of Technology
Masked
Software
Masked
Hardware
UMA
Notes: Before I’m actually going to start this talk with a brief discussion on why we think that it was about time

## Slide 2: In this work…
Unified Masking Approach (UMA)
  combines SW & HW
  randomness
  shares
  generic,
  glitch resistant
HW case study
  Ascon
  UMA vs. DOM
  single & 64 S-box
  results for
  github.com/hgrosz
Q: “Does randomness reduction pay off?”
Notes: In this work we had a closer look on..
To demonstrate how these properties map..

## Slide 3: A Brief History of Boolean Masking
DPA
1999
(1 AK)
Masking
ChariJRR99
GoubinP99
EMA
(QuisquaterS01)
Trichina gate & ISW
Trichina03
IshaiSW03
Glitches
MangardPG05
BelaidBPPTV16
8 … 16
… 18
TI scheme
NikovaRR06
HO TI
BilginGNNR14
DOM
GrossMK17
CMS
ReparazBNGV15
BartheDFGSS16
AES d+1 shares
(DeCnuddeRBNNR16)
17 18
1 3 5 7 9 11 13 15 17 19
MIND THE GAP
Notes: I want to begin my actual talk with a brief historical overview on…
Anno Domini… Anno Kocher…
Eurocrypt 2016 of Bela-i-d
and the Bounded Moment Leakage Model of Barthe et al.

## Slide 4: How big is the randomness gap?
Chart: 
lower bound | 1 | 2 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
best SW | 1 | 2 | 4 | 5 | 11 | 14 | 16 | 18 | 29 | 33 | 36 | 39 | 55 | 60 | 64
Belaïd et al.’s optimal solutions
Barthe et al.’s generic algorithm
Belaïd et al.’s generic algorithm
randomness
protection order (d)
Notes: How big is the randomness gap between Software and Hardware Based Masking
Lower bound:
d 1… 2  d randomness
d 3…  d+1 randomness
tightness??
best SW: best of optimal solutions from Belaid, and generic variants of Belaid and Barthe

## Slide 5: How big is the randomness gap?
Chart: 
lower bound | 1 | 2 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
DOM | 1 | 3 | 6 | 10 | 15 | 21 | 28 | 36 | 45 | 55 | 66 | 78 | 91 | 105 | 120
best SW | 1 | 2 | 4 | 5 | 11 | 14 | 16 | 18 | 29 | 33 | 36 | 39 | 55 | 60 | 64
twice the randomness
randomness
protection order (d)
Notes: add UMA
DOM
Biggest gap at points where d = integral multiple of 4
were are not only closing this gap, but improve on Barthe\Belaid et al’s algorithms for d = 1 mod 4

## Slide 6: Masked Multiplication
(d+1)² terms
Notes: When I talk about randomness requirements I refer to the simplest nonlinear…
Multiplication results in sharing in (d+1)² terms  no randomness, secure when sharing of a and b independent  story could be over here
All resulting terms are not allowed to come together  violation of d-probing model

## Slide 7
…
Masked Multiplication
Notes: Exponential growth in number of terms\shares…. (d+1)² x (d+1)  (d+1)³
 still no randomness required when inputs

## Slide 8
Compressing
Notes: Reduce number of terms to d+1 again by summing up these terms
None of these terms are allowed to come together in a direct manner
Therefore fresh random bits are required. But what is the most efficient way to perform this reduction?
Main difference in SW … how many fresh random bits. in HW, also how much controll over combination sequence is requried?

## Slide 9
Barthe et al.’s Generic Algorithm
Chart: 
Notes: Absorbtion of terms as repeating sequence
state that SINE is a symbol for repeating sequence

## Slide 10
Example for
Barthe et al.‘s algorithm
Domain-Oriented Masking
Notes: Example for first-order
Bathe et al‘s algorithm works quite well for Complete sequences…

## Slide 11
Chart: 
Chart: 
Complete
Sequence Types
Pseudo-Complete
Half-Complete
Incomplete
Notes: As it shows, Barthes algorithm is most efficient if 4 terms are absorbed…
Multiple sequences of type „complete“ (four terms per domain absorbed)  Barthe et al‘s algorithm
Psuedo-complete  treat the same as complete sequences
Half-complete  DOM
same randomness as Barthe‘s, but better suitablility in HW
Incomplete  DOM

## Slide 12
inner-domain terms
complete sequences
last sequence
pseudo-complete
half-complete
incomplete
Belaïd et al.
Barthe et al.
DOM
Notes: With this in mind we can begin to implement UMA in Software..

## Slide 13
UMA in Hardware
Following DOM paradigm
Split into submodules
Domain separation
Constant latency ()
Notes: For the implementation in Hardware we followed the design principles of DOM…
Construction of a Masked AND gate following the DOM principles

## Slide 14: Back to the Randomness Gap
randomness
protection order
Chart: 
lower bound | 1 | 2 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
DOM | 1 | 3 | 6 | 10 | 15 | 21 | 28 | 36 | 45 | 55 | 66 | 78 | 91 | 105 | 120
UMA | 1 | 2 | 4 | 5 | 9 | 14 | 16 | 18 | 25 | 33 | 36 | 39 | 49 | 60 | 64
best SW | 1 | 2 | 4 | 5 | 11 | 14 | 16 | 18 | 29 | 33 | 36 | 39 | 55 | 60 | 64
Notes: We not only closed the gap but also improved on SW
d = 5 : UMA 9 vs 12 in SW  save 3 (25%)
d = 9 : UMA 25 vs 30 in SW  save 5
d = 13 : UMA 49 vs 56 in SW  save 7
add UMA
DOM
Biggest gap at points where d = integral multiple of 4
were are not only closing this gap, but improve on Barthe\Belaid et al’s algorithms for d = 1 mod 4

## Slide 15
Ascon - Case Study
AE scheme
Round 3 CAESAR candidate
128-bit key & nonce
64 or 128 bit rate
1-64 S-boxes (5-bit)
generic protection
pipelined
Notes: To have a fair comparison between DOM and UMA under real-world conditions…
Main functionality in State
S-box very compact
Comparison for different amounts of nonlinearity

## Slide 16
Area: Ascon-Single Sbox
Chart: 
DOM1 | 10854.5918 | 16185.9056 | 21585.7781 | 27124.3622 | 32757.3342 | 38423.1505 | 44255.4209 | 50200.8929 | 56139.3495 | 62401.148 | 68527.7423 | 74882.6531 | 81193.8776 | 87748.7245 | 94235.3316
LR1 | 10828.125 | 16373.4056 | 22133.9286 | 27861.2883 | 33639.3495 | 39437.8189 | 45940.3699 | 51954.7194 | 58116.0714 | 64324.9362 | 71523.2781 | 77962.3724 | 84549.426 | 91522.6403 | 99048.1505
DOM1 | 10854.5918 | 16185.9056 | 21585.7781 | 27124.3622 | 32757.3342 | 38423.1505 | 44255.4209 | 50200.8929 | 56139.3495 | 62401.148 | 68527.7423 | 74882.6531 | 81193.8776 | 87748.7245 | 94235.3316
LR1 | 10828.125 | 16373.4056 | 22133.9286 | 27861.2883 | 33639.3495 | 39437.8189 | 45940.3699 | 51954.7194 | 58116.0714 | 64324.9362 | 71523.2781 | 77962.3724 | 84549.426 | 91522.6403 | 99048.1505
DOM1 | 10854.5918 | 16185.9056 | 21585.7781 | 27124.3622 | 32757.3342 | 38423.1505 | 44255.4209 | 50200.8929 | 56139.3495 | 62401.148 | 68527.7423 | 74882.6531 | 81193.8776 | 87748.7245 | 94235.3316
LR1 | 10828.125 | 16373.4056 | 22133.9286 | 27861.2883 | 33639.3495 | 39437.8189 | 45940.3699 | 51954.7194 | 58116.0714 | 64324.9362 | 71523.2781 | 77962.3724 | 84549.426 | 91522.6403 | 99048.1505
DOM1 | 10854.5918 | 16185.9056 | 21585.7781 | 27124.3622 | 32757.3342 | 38423.1505 | 44255.4209 | 50200.8929 | 56139.3495 | 62401.148 | 68527.7423 | 74882.6531 | 81193.8776 | 87748.7245 | 94235.3316
LR1 | 10828.125 | 16373.4056 | 22133.9286 | 27861.2883 | 33639.3495 | 39437.8189 | 45940.3699 | 51954.7194 | 58116.0714 | 64324.9362 | 71523.2781 | 77962.3724 | 84549.426 | 91522.6403 | 99048.1505
DOM1 | 10854.5918 | 16185.9056 | 21585.7781 | 27124.3622 | 32757.3342 | 38423.1505 | 44255.4209 | 50200.8929 | 56139.3495 | 62401.148 | 68527.7423 | 74882.6531 | 81193.8776 | 87748.7245 | 94235.3316
LR1 | 10828.125 | 16373.4056 | 22133.9286 | 27861.2883 | 33639.3495 | 39437.8189 | 45940.3699 | 51954.7194 | 58116.0714 | 64324.9362 | 71523.2781 | 77962.3724 | 84549.426 | 91522.6403 | 99048.1505
DOM1 | 10854.5918 | 16185.9056 | 21585.7781 | 27124.3622 | 32757.3342 | 38423.1505 | 44255.4209 | 50200.8929 | 56139.3495 | 62401.148 | 68527.7423 | 74882.6531 | 81193.8776 | 87748.7245 | 94235.3316
LR1 | 10828.125 | 16373.4056 | 22133.9286 | 27861.2883 | 33639.3495 | 39437.8189 | 45940.3699 | 51954.7194 | 58116.0714 | 64324.9362 | 71523.2781 | 77962.3724 | 84549.426 | 91522.6403 | 99048.1505
[kGE]
UMA
DOM
protection order
Notes: area results are quit similar: - because UMA  less randomness  less XORs

## Slide 17
Area: Ascon-64 S-box
[kGE]
UMA
Chart: 
 | 28887.4362 | 52995.2168 | 81208.8648 | 118263.7117 | 161869.898 | 207715.5612 | 263918.3673 | 327217.1556 | 390676.6582 | 473915.4974 | 549541.4541 | 638821.1097 | 725993.6224 | 828183.3546 | 926331.6327
 | 27176.6582 | 65465.8801 | 117720.3444 | 168000.3189 | 220094.3878 | 274932.398 | 373110.0128 | 445196.1097 | 521158.801 | 603845.3444 | 747012.7551 | 841998.4056 | 953384.5663 | 1085008.9286 | 1252461.0969
protection order
DOM
Notes: One-Sbox variant
64-Sboxes in parallel
Ready & Busy signaling… e.g. AXI4 streaming device
Main functionality in State
S-box very compact
Comparison for different amounts of nonlinearity

## Slide 18
Throughput: Ascon-Single Sbox
[Mb/s]
Chart: 
 | 108.1549 | 104.9487 | 105.8936 | 67.159 | 89.266 | 80.2536 | 74.7437 | 61.6221 | 59.8545 | 60.7746 | 56.1625 | 69.2326 | 66.5639 | 49.2734 | 47.5878
 | 108.1549 | 108.0815 | 110.0235 | 71.1685 | 94.5954 | 84.5481 | 80.2844 | 63.1511 | 62.2134 | 63.9887 | 70.9149 | 72.7956 | 70.1339 | 70.6004 | 50.4289
UMA
protection order
DOM
Notes: Sigle Sbox variants: between 100 and 50 Mbps
402 vs 426 cycles
18 vs 42 cycles

## Slide 19
Throughput: Ascon-64 S-box
[Mb/s]
Chart: 
 | 108.1549 | 104.9487 | 105.8936 | 67.159 | 89.266 | 80.2536 | 74.7437 | 61.6221 | 59.8545 | 60.7746 | 56.1625 | 69.2326 | 66.5639 | 49.2734 | 47.5878
 | 108.1549 | 108.0815 | 110.0235 | 71.1685 | 94.5954 | 84.5481 | 80.2844 | 63.1511 | 62.2134 | 63.9887 | 70.9149 | 72.7956 | 70.1339 | 70.6004 | 50.4289
 | 2246.0869 | 1091.2191 | 897.4143 | 805.8221 | 845.6213 | 756.233 | 802.8501 | 894.2544 | 615.432 | 576.1095 | 540.9334 | 660.5156 | 691.6975 | 580.9415 | 525.6328
 | 2246.0869 | 1896.2963 | 1903.4023 | 1785.8139 | 1868.3949 | 1809.443 | 1366.4702 | 1652.2098 | 1702.8523 | 1573.2547 | 1743.7742 | 1497.076 | 1832.7606 | 1438.9136 | 1479.6319
 | 2246.0869 | 1091.2191 | 897.4143 | 805.8221 | 845.6213 | 756.233 | 802.8501 | 894.2544 | 615.432 | 576.1095 | 540.9334 | 660.5156 | 691.6975 | 580.9415 | 525.6328
Single S-box variants
UMA
protection order
DOM
Notes: 402 vs 426 cycles
18 vs 42 cycles

## Slide 20: But didn’t we forget something…?
Which RNG?
Ascon as PRNG (GrossWDE15)
  64 bits every 6 cycles
  + 7.1 kGE
Randomness bottleneck
  DOM from
  UMA from
Chart: 
DOM | 1 | 2 | 3 | 5 | 8 | 10 | 14 | 17 | 22 | 26 | 31 | 37 | 43 | 50 | 57
UMA | 1 | 1 | 2 | 3 | 6 | 7 | 8 | 9 | 14 | 16 | 17 | 19 | 26 | 29 | 30
UMA
#PRNGs
protection order
DOM
Notes: Numbers from before do not reflect the effort for producing random numbers
Number of PRNGs given for Single- S-box variant
Randomness becomes bottleneck  need more PRNGs

## Slide 21: Area with Randomness Costs
[kGE]
protection order
UMA
Chart: 
DOM1SBOX
UMA1SBOX


DOM1SBOX | 17.9546 | 30.3859 | 42.8858 | 62.6244 | 89.5573 | 109.4232 | 143.6554 | 170.9009 | 212.3393 | 247.0011 | 288.6277 | 337.5827 | 386.4939 | 442.7487 | 498.9353
UMA1SBOX | 17.9281 | 23.4734 | 36.3339 | 49.1613 | 76.2393 | 89.1378 | 102.7404 | 115.8547 | 157.5161 | 177.9249 | 192.2233 | 212.8624 | 269.1494 | 297.4226 | 312.0482
DOM64Sbox | 241.8874 | 691.9952 | 1359.2089 | 2248.2637 | 3356.8699 | 4680.7156 | 6227.9184 | 7995.2172 | 9975.6767 | 12188.9155 | 14607.5415 | 17252.8211 | 20108.9936 | 23193.1834 | 26486.3316
UMA64Sbox | 240.1767 | 491.4659 | 969.7203 | 1233.0003 | 2563.0944 | 3256.9324 | 3781.11 | 4279.1961 | 6698.1588 | 7632.8453 | 8415.0128 | 9148.9984 | 12668.3846 | 13865.0089 | 14884.4611
Single S-box variants
DOM
Notes: Numbers from before do not reflect the effort for producing random numbers
Number of PRNGs given for Single- S-box variant
 for 64-bit parallel

## Slide 22: Conclusions
Introduction of UMA
  masking in SW and HW
  ~d(d+1)/4 randomness
UMA vs. DOM masked Ascon
  generic protection
  customizable (rate, S-Boxes, rounds, …)
  github.com/hgrosz
  including Ascon, AES, Keccak, RISC-V, …
Randomness reduction does pay off
  randomness = bottleneck
  save randomness  save area  increase throughput
UMA
Notes: Today I had the great pleasure to introduce UMA…
-closes randomness gap in SW and improves on it
Umkehrschluss  consider the reverse conclusion

## Slide 23: Reconciling d + 1 Masking in Hardware and Software
Hannes Gross, Stefan Mangard
Graz University of Technology
Masked
Software
Masked
Hardware
UMA

## Slide 24: Masking - Linear Operations
Notes: Result of linear operation is again a d+1 sharing of the result

## Slide 25: Efficiency Comparison
[Mbps/kGE]
protection order
UMA
DOM
Single S-box variants
Chart: 




 | 6.0238 | 3.557 | 2.5655 | 1.1364 | 1.0563 | 0.77267 | 0.55887 | 0.36952 | 0.29299 | 0.25906 | 0.2457 | 0.21564 | 0.18146 | 0.15946 | 0.10107
 | 6.0327 | 4.471 | 2.9145 | 1.3661 | 1.1709 | 0.90033 | 0.7275 | 0.53189 | 0.37999 | 0.34157 | 0.29217 | 0.32525 | 0.24731 | 0.16567 | 0.1525
 | 9.2857 | 2.7403 | 1.4004 | 0.79431 | 0.55659 | 0.38657 | 0.21941 | 0.20665 | 0.1707 | 0.12907 | 0.11937 | 0.086773 | 0.091141 | 0.06204 | 0.055864
 | 9.3518 | 2.2203 | 0.92544 | 0.65355 | 0.32992 | 0.23219 | 0.21233 | 0.20898 | 0.091881 | 0.075478 | 0.064282 | 0.072195 | 0.0546 | 0.0419 | 0.035314
Notes: Single S-box variants more efficient
UMA more efficient
For high-throughput DOM more efficient, but circuit size is overwhelming

## Slide 26: A Brief History of Boolean Masking
DPA
1999
1 AK
Masking
ChariJRR99
GoubinP99
EMA
(QuisquaterS01)
Trichina gate & ISW
Trichina03
IshaiSW03
Glitches
MangardPG05
BelaidBPPTV16
8 … 16
… 18
TI scheme
NikovaRR06
HO TI
BilginGNNR14
DOM
GrossMK17
CMS
ReparazBNGV15
BartheDFGSS16
AES d+1 shares
(DeCnuddeRBNNR16)
17 18
1 3 5 7 9 11 13 15 17 19
MIND THE GAP
Notes: Sonia Bela-i-d
Introducing new time
DPA Kocher 0 AK (1999)
masking (ChariJRR99) & GoubinP99 0 AK (1999)
EMA Quisquatter (QuisquaterS01) 2 AK (2001)
Trichina gate (Trichina03) 4 AK (2003)
ISW scheme (IshaiSW03) 4 AK (2003)
Glitches (MangardPG05) 6 AK (2005)
Hardware branch:
TI scheme (NikovaRR06) 7 AK (2006)
...
Bilgin HO TI (BilginGNNR14) 15AK (2014)
Reparaz note on HO TI (Reparaz15) 16AK (2015)
Consolidating Masking (ReparazBNGV15) 16AK (2015)
AES d+1 (CnuddeRBNNR16) 17AK (2016)
DOM (GrossMK16) 17AK (2016)
Software:
Belaid Randomness Complexity... (BelaidBPPTV16) 17 AK (2016)
Barthe Bounded Moment Leakag... (BartheDFGSS17) 18 AK (2017)

## Slide 27
UMA vs. DOM – Area of Masked AND
Chart: 
 | 24 | 68.25 | 134 | 221.25 | 330 | 460.25 | 612 | 785.25 | 980 | 1196.25 | 1434 | 1693.25 | 1974 | 2276.25 | 2600
 | 24 | 76.75 | 142 | 218.75 | 327 | 456.75 | 624 | 776.25 | 970 | 1185.25 | 1446 | 1673.75 | 1953 | 2321.25 | 2608
Chart: 
 | 33 | 81.75 | 152 | 243.75 | 357 | 491.75 | 648 | 825.75 | 1025 | 1245.75 | 1488 | 1751.75 | 2037 | 2343.75 | 2672
 | 42 | 157.75 | 322 | 488.75 | 651 | 834.75 | 1128 | 1343.25 | 1600 | 1878.25 | 2310 | 2609.75 | 2961 | 3401.25 | 3904
[GE]
protection order
UMA
DOM
Notes: For unpipelined AND agtes UMA and DOM requires the same area -> delay for UMA is bigger

## Slide 28
UMA vs. DOM – Randomness of Masked AND
random bits
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
DOM | 1 | 3 | 6 | 10 | 15 | 21 | 28 | 36 | 45 | 55 | 66 | 78 | 91 | 105 | 120
UMA | 1 | 2 | 4 | 5 | 9 | 14 | 16 | 18 | 25 | 33 | 36 | 39 | 49 | 60 | 64
protection order
UMA
DOM
Notes: UMA requires half the randomness of DOM, in case modulus of d is 1 even more efficient than Barthe algorithm

## Slide 29
Summary – Single S-Box Variants
DOM Ascon
10.8 – 94 kGE
5 – 600 random bits/cycle
402 cycles/absorption
108 – 50 Mbit/s
UMA Ascon
10.8 – 99 kGE
5 – 320 random bits/cycle
402-426 cycles/absorption
108 – 48 Mbit/s
C
A
B
Z
…
Notes: Ready & Busy signaling… e.g. AXI4 streaming device
Main functionality in State
S-box very compact
Comparison for different amounts of nonlinearity

## Slide 30
Summary – 64 S-Boxes Variants
DOM Ascon
28 – 926 kGE
320 – 38,400 random bits/cycle
18 cycles/absorption
2.25 – 1.48 Gbit/s
UMA Ascon
28 – 1,252 kGE
320 – 20,480 random bits/cycle
18 – 42 cycles/absorption
2.25 – 0.53 Gbit/s
C
A
B
Z
…
Notes: Ready & Busy signaling… e.g. AXI4 streaming device
Main functionality in State
S-box very compact
Comparison for different amounts of nonlinearity